        TESTBENCH ARCHITECTURE OF I2C PROTOCOL

- I2c is a 2-wire bus. It was invented by Phillips semiconductor.
- The main objective of this testbench is to verify i2c protocol using UVM methodology.
- There are 4 modes in i2c: Master transmitter, master receiver, slave transmitter and slave receiver.
- Testbench architecture is shown below.
- It consists of following blocks: i2c_test, i2c_env, m_i2c_agent, s_i2c_agent, m_i2c_seqr, m_i2c_driver, m_i2c_mon, s_i2c_seqr, s_i2c_driver, s_i2c_mon, i2c_sb, i2c_func_cov.

Steps for WRITE operation:

Master transmitter will send start condition to slave receiver, followed by 7/9 bit slave address, followed by 0 for write operation. Then master transmitter will send 8 bit data to slave receiver in every clock cycle. Then slave receiver will send either ack/nack to master transmitter. Finally, master transmitter will send stop condition to slave receiver to terminate the transfer

Steps for READ operation:

Master receiver sends start condition and address of the slave transmitter. Then master receiver sends the address of slave transmitter followed by1. Master receiver receives the data from slave transmitter. Finally master receiver terminates the transfer by sending stop condition.

i2c_test:
A testcase is a pattern to target checks and verify specific features of a design. It contains environment.

i2c_env:
A UVM environment contains multiple, reusable verification components and defines their default configuration as required by the application. It consists of master i2c agent, slave i2c agent, i2c scoreboard and functional coverage block.

m_i2c_agent:
Master i2c agent basically consists of master i2c sequencer, master i2c driver and master i2c monitor and will make connections between these components through TLM ports. We WILL Configure it as an active agent. The main purpose of this block is to enable data driven to DUT through m_i2c_driver.

m_i2c_sequencer:
Master i2c sequencer is basically an advanced stimulus generator which performs some arbitration on the sequences and then send it to the driver. It will send the transactions to master i2c_driver.

m_i2c_driver:
It receives the transactions from sequencer and drives it to the DUT. Basically it converts the transactions to pin level signals.

m_i2c_monitor:
Master i2c monitor receives the signals from DUT and converts pin levels signals to transactions. It send the transactions to scoreboard and coverage models as well.

s_i2c_agent:
This is slave i2c agent, consists of slave i2c sequencer, slave i2c driver and slave i2c monitor.

s_i2c_sequencer:
Slave i2c sequencer will send the transactions to slave i2c driver through TLM ports.

s_i2c_driver:
 Slave i2c_driver will drive the signals to the DUT through virtual interface.

s_i2c_monitor:
Slave i2c monitor will receives the pin level signals from DUT converts them back to transactions and sends them to scoreboard and coverage model.

i2c_scoreboard:
i2c scoreboard will compare actual and expected data.

i2c_test seq seq

i2c_sb
i2c_env

i2c_func_cov
s_i2c_seqr

        m_i2c_agent s_i2c_agent

m_i2c_driver

DUT
Virtual interface
Virtual interface

m_i2c_seqr
m_i2c_monitor

s_i2c_monitor

s_i2c_driver